## Slide 1: Applied Electricity (ELNG 103) 3 credit
Nana Twum Duah
Email: nana.twumduah@yahoo.com
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
UENR
Notes: Click to add notes

## Slide 2: Teaching and Assessment
Lectures:
Tutorials:
Assessment:
One mid- term test
Assignments
Exams
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 3: Contents
Fundamentals of electricity
Network Theorems (DC)
Alternating Voltage and Current
A.C. Circuits
Magnetic Circuits
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 4: Reference Books
Hughes E. , Electrical and Electronics Technology
Theraja B.L, Theraja R.K, A Text Book of Electrical Technology
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 5: Aim and Objective
Understand and apply fundamental network theorems in DC circuits.
Known the basics of AC parameters – single and three phase introduced.
Magnetic Circuits
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 6: details- fundamentals of electricity
Fundamentals of electricity
Electricity
Electric Charge
Current
Voltage
Resistance
Power
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 7: Introduction
Fundamentals of electricity
Electricity is the flow of electric charges in a circuit
Electric charge Q (coulomb): quantity of electricity passing a given point in a circuit when a current of 1 A is maintained for 1 sec.
Q = I x t
Current I (amperes) : flow rate of electrical charge (1 A = 1 C/s)
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 8: Introduction
Voltage V (volts): electrical potential difference - energy absorbed or released per coulomb of charge moving from point to another (1 V = 1 J/C).
Resistance R (ohms Ω): degree to which an electrical component (resistor) opposes the flow of electric current.
Power P (watts): rate of energy flow (1 W = 1 J/s)
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
Notes: Lesson descriptions should be brief.

## Slide 9: Introduction
e.g.
The electrical potential of point A is 200 V higher than that of point B, and 30 C of charge per minute flows from A to B. Determine the current and power flow from A to B and the energy transferred in 1 min.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 10: Part A.
Basic electric system
Ohms Law
D.C circuit
Kirchoff’s laws
Resistors in series and parallel
Superposition and Reciprocity theorems
Thevenin’s and Norton’s theorems
Delta-star and star-delta transformations
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 11: Basic electric system
Source: Provide energy for the electrical system. e.g. battery, generator
Load: absorb electrical energy supplied by the source. e.g. home appliance such as lamps, heaters, TV.
Transmission system: conducts energy from the source to the load. Mostly consist of wire/cable.
Control apparatus: controls the system. e.g. switch
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 12: Basic electric system
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 13: Ohms Law
The law states that the strength of a current is directly proportional to the voltage and inversely proportional to resistance offered.
If I, V and R be expressed in terms of units,
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 14: Ohms Law
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 15: Ohms Law
R can range from zero to infinity, it is important that we consider the two extreme possible values of R.
Short circuit – when R=0,
i.e. voltage is zero but the current could be anything.
Open Circuit – R = ∞,
i.e. current is zero but the voltage could be
anything
.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 16: Ohms Law
Power
The power dissipated by a resistor can be expressed in terms of R:
The power dissipated in a resistor is a nonlinear function of either current or voltage.
Since R is positive quantities, the power dissipated in a resistor is always positive. Thus, a resistor always absorbs power from the circuit.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 17: DC circuit
Direct current (DC) is current that flow in unidirectional. Sources - batteries, solar cells
Constant DC b. Variable DC
DC circuit is a circuit that Electric Current flows through in one direction.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 18: Network Theorems
Kirchhoff’s Laws
Current law: At any junction in an electric circuit the total current flowing towards that junction is equal to the total current flowing away from the junction. i.e.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
Notes: where N is the number of branches connected to the node and In is the nth current entering (or leaving) the node

## Slide 19: Kirchhoff’s Laws
Voltage Law: In any closed loop in a network, the algebraic sum of the voltage drops taken around the loop is equal to the resultant e.m.f. acting in that loop.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 20: Application of Kirchhoff’s Laws
e.g. find each branch current and voltage drop across each resistor in the network.
a. b.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
Notes: Solution
Current flowing through R1=6.52A, R2=6.37A and R3=0.15A
I1= 3A, I2 =1A, V1 = 24V, V2 =6V V3 =6V

## Slide 21: Application of Kirchhoff’s Laws
Try. find each branch current and voltage drop across each resistor in the network
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 22: Resistors in series & Voltage division
The two resistors are in series, since the same current i flows in both of them.
Applying ohm’s law
Apply KVL
where
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 23: Resistors in series & Voltage division
The equivalent resistance of any number of resistors connected in series is the sum of the individual resistances.
For N resistors in series then,
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 24: Resistors in series & Voltage division
Voltage division
Substituting (2) into (1)
In general, if a voltage divider has N resistors (R1 , R2 , . . . , RN ) in
series with the source voltage v, the nth resistor (Rn) will have a voltage drop of
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 25: Parallel resistors and current division
When two resistors are connected in parallel – have the same voltage across them.
From ohms,
Rearranging
Applying KCL at node a
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 26: Parallel resistors and current division
Therefore,
Substituting (6) into (7)
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
Notes: Equation (10) applies only to two resistors in parallel.
If R1 = R2 , then, Req= R1/2

## Slide 27: Parallel resistors and current division
The equivalent resistance of two parallel resistors is equal to the product of their resistances divided by their sum.
For N number of resistors in parallel,
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 28: Parallel resistors and current division
Combining (6) and (11)
Current division
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 29: Resistance in series and parallel
Find the total resistance as seen from terminal AB
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 30: Resistance in series and parallel
Find the total resistance as seen from terminal AB
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 31: Superposition theorem
states that the voltage across or current through an element in a linear circuit is the algebraic sum of the voltage across or currents through that element due to each independent source acting alone.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 32: Superposition theorem
Steps to Apply Superposition Principle:
Turn off all independent sources except one source. Find the output (voltage or current) due to that active source.
Repeat step 1 for each of the other independent sources.
Find the total contribution by adding algebraically all the contribution due to the independent sources.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 33: Superposition theorem
e.g. Use the superposition theorem to find v in the circuit in the networks.
a. b.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
Notes: Solution
a. V = 10V
B. VO= 12V

## Slide 34: Superposition theorem
Try. Use superposition theorem to find the current i.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
Notes: i = 2A

## Slide 35: Reciprocity Theorems
The reciprocity theorem is applicable only to single-source networks and states the following:
The current I in any branch of a network, due to a single voltage source E anywhere in the network, will equal the current through the branch in which the source was originally located if the source is placed in the branch in which the current I was originally measured
The location of the voltage source and the resulting current may be interchanged without a change in current
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 36: Reciprocity Theorems
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 37: Reciprocity Theorems
E.g. Using reciprocity theorem find the ammeter current.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 38: Source transformation
Is a tool for simplifying electric circuits.
A source transformation is the process of replacing a voltage source vs in series with a resistor R by a current source is in parallel with a resistor R, or vice versa.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 39: Source transformation
E.g. Use source transformation to find vo in the circuit.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
Notes: Solution
Vo = 3.2V

## Slide 40: Thevenin’s theorem
Thevenin’s theorem states that a linear two-terminal circuit can be replaced by an equivalent circuit consisting of a voltage source VTh in series with a resistor RTh, where VTh is the open-circuit voltage at the terminals and RTh is the input or equivalent resistance at the terminals when the independent sources are turned off.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 41: Thevenin’s theorem
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 42: Thevenin’s theorem
Procedure
Remove the load resistance from that branch.
Determine the open-circuit voltage, Vth, across the break.
Remove each Voltage and current sources and replace them by their internal resistan- ces and then determine the resistance, Rth, ‘looking-in’ at the break. i.e. replace voltage source with short circuit and current source with open circuit.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 43: Thevenin’s theorem
4. Obtained the thevenin equivalent circuit
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 44: Thevenin’s theorem
e.g. Find the Thevenin equivalent circuit of the circuit shown in to the left of the terminals a-b. Then find the current through RL = 6, 16, and 36 .
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
Notes: Solution
Rth = 4Ω
Vth = 30V
When RL= 6Ω, 16Ω and 36Ω.
IL=3A, 1.5A, 0.75A respectively

## Slide 45: Thevenin’s theorem
e.g. Using Thevenin’s theorem, If the galvano- meter has a resistance of 40Ω , find the current through the galvanometer.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
Notes: Vth = 77V
Rth = 990Ω

## Slide 46: Thevenin’s theorem
Try. Using Thevenin’s theorem, find the equivalent circuit to the left of the
terminals in the circuit. Then find i
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING
Notes: Vth= 6V
Rth=3Ω
i = 1.5A

## Slide 47: Norton’s Theorem
Norton’s theorem states that a linear two-terminal circuit can be replaced by an equivalent circuit consisting of a current source IN in parallel with a resistor RN, where IN is the short-circuit current through the terminals and RN is the input or equivalent resistance at the terminals when the independent sources are turned off.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 48: Thevenin’s theorem
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 49: Thevenin’s theorem
Procedure
Remove the load resistance from that branch.
Determine the short-circuit current, isc, flowing from terminal a to b.
Remove each Voltage and current sources and replace them by their internal resistan- ces and then determine the resistance, RN, ‘looking-in’ at the break. i.e. replace voltage source with short circuit and current source with open circuit.
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 50: Thevenin’s theorem
4. Obtained the Norton’s equivalent circuit
Electrical and Electronic Engineering
SCHOOL OF ENGINEERING

## Slide 51
,.,,